## Slide 1
Chapter 5, Basic OOP topics
Why OOP
OOP terminology
Classes
Objects
Custom constructors
Static variables/methods
Classes within classes
Handles
Copying objects
Notes: Why OOP: Why it is worth learning and using the class based features of SystemVerilog
OOP Terminology: OOP uses terms like class, object, handle, methods, and properties. Need to be comfortable with these terms.
Classes: How to create a class
Objects: How objects are created.
Custom constructors: How to overload the default constructor with a custom constructor
Static variables/methods: How to create a variable that is shared by any object of a class. Use a static method to manipulate static variables
Classes within classes: Can create objects of another class inside of a class
Handles: Modifying handles, arrays of handles, etc.
Copying objects: Shallow copy vs. deep copy

## Slide 2
5.1 Introduction
Why OOP?
Gains in productivity/maintainability/thoroughness
Strongly couples data with code that manipulates it.
Allows the testbench to be reused
Facilitates testing at the transaction level
SystemVerilog allows inheritance and polymorphism
Notes: START: Why it is worth learning and using the class based features of SystemVerilog
1) Gains in productivity/maintainability/thoroughness using object oriented concepts from S/W engineering
2) Strongly couples data with code that manipulates it because the tasks/functions are in the same class that the data is declared.
3) Allows the Testbench to be reused because OOP decouples the testbench from design details making it more general and easier to maintain and reuse
4) Facilitates testing at the transaction level: The data that flows in and out of the design is grouped together in transactions so the easiest way to organize the testbench is around the transactions and the operations that you perform
5) Inheritance allows for extending the characteristics & functionality of existing classes. Polymorphism is a lot like templatization in C++.

## Slide 3
5.2 Think of Nouns, not Verbs
Notes: 1) This is how a traditional testbench was created. Everything centered around actions or operations that had to happen
2) We saw this figure from the first class. Instead of actions think of creating objects that do actions. Divide the testbench into blocks and define how they communicate.

## Slide 4: 5.5 OOP Terminology
Blueprint for a house
Class
A complete house
Object
123 Elm Street
House Address
Handle
Light switches
Properties
Turn on/off switches
Methods
Dr. Meeta Yadiv, ASIC Verification, North Carolina State University Fall 2007
Notes: 1) The class is a blueprint of a house. This plan describes the structure of the house, but you cannot live in a blueprint you need to physically build the house.
2) An object is the actual house. Just like a blueprint can be used over and over a class can be called over and over to create lots of objects.
3) The handle, or pointer in C++ terminology, of the house is the address. It uniquely identifies the house (object).
4) Inside the house are things to manipulate like light switches. In SystemVerilog they are called properties. In Verilog they would be called variables and in C++ would be called data members.
5) The action to turn on/off the switches is done by methods. In Verilog this is done in tasks, functions, initial, and always blocks. In C++ these would be called member functions.

## Slide 5: 5.5 OOP Terminology (cont)
Class
  Programming element “containing” related groups of features and functionality
  Provides a template for building objects
  Can be used as a data structure
Object
  An object is an instance of a class
Handle
  Type-safe pointer to an object – can not be corrupted
Properties
  Variables contained in the instance of the class
Methods
  Tasks/functions (algorithms) that operate on the properties in this instance of the class
Blueprint for a house
A complete house
Light switches
Turn on/off switches
Address of a house
Dr. Meeta Yadiv, ASIC Verification, North Carolina State University Fall 2007
Notes:   Type-safe pointer to an object – cannot be corrupted because a SystemVerilog handle can only point to objects of one type, unlike in C. We’ll talk more about SystemVerilog’s handle allocation and garbage collection in a few slides.

## Slide 6: 5.5 OOP Terminology (cont)
Dr. Meeta Yadiv, ASIC Verification, North Carolina State University Fall 2007
Notes: This slide compares Verilog programming constructs with OOP using SystemVerilog

## Slide 7
5.3 Your First Class
class Transaction;
bit [31:0] addr, crc, data[8];
function void display;
  $display(“Transaction: %h”, addr);
  endfunction
  fuction void calc_crc;
  crc = addr ^ data.xor;
  endfunction
endclass
: display
: calc_crc
: Transaction
properties or variables
method
method
Notes: 1) This is sample 5.1 which creates a class for a generic transaction. The contents of the transaction are a 32-bit address and crc and an array of 8 32-bit words called data. The transaction class has two functions, one which displays the address of the transaction and the other which does a bitwise xor on the data array using the xor method and then xor’s it with the address of the transaction. At this point it looks a lot like a module.
2) In the book the authors label the endfunction and the endclass to match the beginning and end of a block. Use this if you find it helpful.

## Slide 8
5.4 Where to define (and use) a Class
A class can be defined in:
program
module
package
A class can be used in:
module
program
package
Can be constructed and extended
Locations for defining classes:
  Each class in a separate file
  Related classes in a package
Notes: Recommendation is to locate each class in a separate file unless you expect the # to get too large. In that case group related classes in a package.

## Slide 9
5.6 Creating new objects
Transaction tr;
tr = new();
class
handle
creates an object of class Transaction
tr now points to the object
Transaction tr = new();
OR
Call new() to allocate space for the object
Notes: 1) Transaction is the class we declared earlier.
2) Transaction tr; declares a handle that can point to objects of type Transaction. At this point we cannot do anything with the handle or the class. Just like a module, a class doesn’t do anything until it’s been instantiated (i.e. space has been allocated for it).
3) When new is called the Transaction object is constructed and space is allocated for class Transaction. tr hold the address of where the object is stored. For every class SystemVerilog creates a default new to allocate and initialize an object.
4) Or this can all be done in 1 line.

## Slide 10
Class in a package
package abc;
class Transaction;
// Class body
endclass
endpackage
program automatic test;
import abc::*;
Transaction tr;
// Test code
endprogram
Notes: A common location for classes is in a package.
In this example class transaction is defined in package abc.
In the program the package is imported and a handle to class Transaction, tr, is declared.

## Slide 11
Class Exercise
Create a class called MemTrans that contains the following members:
  An 8-bit data_in of logic type
  A 4-bit address of logic type
  A void function that prints out the value of data_in and address
Construct a MemTrans object in an initial block
Notes: See Chap_5_Basic_OOP/exercise1 for complete code example.
class MemTrans;
logic [7:0] data_in;
logic [3:0] address;
function void print;
$display(“Data_in = %h, address = %h”, data_in, address);
endfunction
endclass
initial begin
MemTrans MyMemTrans;
MyMemTrans = new();
end
// or
initial begin
MemTrans MyMemTrans = new();
end

## Slide 12
5.6.2 Custom Constructor
For every class SystemVerilog creates a default new()
  Memory space is allocated
  All variables initialized to their default value
Use a custom constructor to override this behavior
class Transaction;
  logic [31:0] addr, crc, data[8];
function new();
addr = 3;
data = '{default:5};
endfunction
endclass
Notes: 1) Without a custom constructor addr, crc, and data would be initialized to X (the default for logic types).
2) Use a custom constructor to override this behavior: essentially overloading new();
The new function sets addr to 3 and every 32-bit word in data to 5 and leaves crc at it’s default value of X.

## Slide 13
Custom Constructor Exercise
Using your MemTrans class create a custom constructor so that data_in and address are both initialized to 0.
Notes: See Chap_5_Basic_OOP/exercise2 for complete code example.
class MemTrans;
logic [7:0] data_in;
logic [3:0] address;
function void print;
$display(“Data_in = %h, address = %h”, data_in, address);
endfunction
function new;
data_in = 8’h0;
address = 4’h0;
endfunction
endclass

## Slide 14
5.6.2 Custom Constructor with arguments
Make the custom constructor more flexible by passing in values
Defaults are used if argument(s) are not passed
class Transaction;
    logic [31:0] addr, crc, data[8];
  function new(logic [31:0] a=3, d=5);
    addr = a;
    data = '{default:d};
  endfunction
endclass
tr1 = new(10);
tr2 = new(, 6);
tr3 = new(10, 6);
tr4 = new(.a(10), .d(6));
Notes: class Transaction: In this constructor if new is called with no arguments the defaults are used.
tr1, tr2, tr3, tr4 are handles to an object of class Transaction
Usage is just like calling a function with default values. Can call by position or by name.

## Slide 15
Custom Constructor with args Exercise
Using your MemTrans class create a custom constructor so that data_in and address are both initialized to 0 but can also be initialized through arguments passed into the constructor
Create 2 new MemTrans objects
Initialize address to 2 in the 1st object, passing arguments by name
Initialize data_in to 3 and address to 4 in the 2nd object, passing arguments by name.
Notes: See Chap_5_Basic_OOP/exercise3 for complete code example.
class MemTrans;
logic [7:0] data_in;
logic [3:0] address;
function void print;
$display(“Data_in = %h, address = %h”, data_in, address);
endfunction
function new(logic [7:0] data_init = 0, logic [3:0] address_init = 0);
data_in = data_init;
address = address_init;
endfunction
endclass
initial begin
MemTrans mt1, mt2;
mt1 = new(.address_init(2));
mt2 = new(.data_init(3), .address_init(4));
end

## Slide 16
5.7 Object Deallocation
Garbage collection, i.e. reclaiming unused memory, is automatic
An object is deallocated if no handles point to it.
t1 = null, t2=null
t2=null, t1
t2
t2 t1
t2 t1 = null
Object A
Object A
Object B
Object A
Object B
Transaction t1, t2;
t1 = new();
t2 = t1;
t1 = new();
t1 = null;
Notes: SystemVerilog’s memory management is automatic, more like Java then C++.
After executing t2 = t1, t2 points to the same object as t1, Object A
After executing t1 = new(), t1 points to a newly created object, Object B. t2 still points to Object A
After executing t1=null, t1 points to nothing (i.e. null). t2 still points to Object A

## Slide 17
class Transaction;
  bit [31:0] addr, crc, data[8];
  function void display;
  $display(“Transaction: %h”, addr);
  endfunction
  fuction void calc_crc;
  crc = addr ^ data.xor;
  endfunction
endclass
Transaction t;
t = new();
t.addr = 32’h42;
t.display();
5.8 Using Objects
Similar to Verilog use the “.” notation to access variables and routines of a class
Usage:
Notes: 1) t.addr accesses variable addr in the object pointed to by t.
2) t.display calls the display function in the object pointed to by t. The current value of addr in the object pointed to by t is displayed.

## Slide 18
Using Objects Exercise
Using the previous MemTrans exercise assign the address of the first object to 4’hF after construction
Use the print function to print out the values of data_in and address for the 2 objects.
Explicitly deallocate the 2nd object.
Notes: See Chap_5_Basic_OOP/exercise4 for complete code example.
class MemTrans;
logic [7:0] data_in;
logic [3:0] address;
function void print;
$display(“Data_in = %h, address = %h”, data_in, address);
endfunction
function new(logic [7:0] data_init = 0, logic [3:0] address_init = 0);
data_in = data_init;
address = address_init;
endfunction
endclass
initial begin
MemTrans mt1, mt2;
mt1 = new(, .address_init(2));
mt2 = new(3, 4);
m1.address = 4’hF;
mt1.print;
$display("-------------------");
mt2.print;
mt2 = null;
end

## Slide 19
class PCI_Tran;
bit [31:0] addr, data;
extern function void display();
endclass
function void PCI_Tran::display();
$display(“%0t: PCI: addr = %h, data = %h”,
$time, addr, data);
endfunction
5.10 Defining Methods Outside of the Class
Done to keep the class definition readable
Define a prototype of the method in the class
Use the extern keyword to indicate the full definition is external
Specify the class that the function is defined for
Notes: 1) f the class contains many long methods the class can span many pages of code and become difficult to follow.
2) Use the extern keyword to indicate the full definition is external to the class definition.
3) If you forget to specify the class that the function is defined for it is defined for the current scope which is probably not what you want. Defining a function to be external and then not defining the function is a compiler error in modelsim.
NOTE: Skip if low on time.

## Slide 20
5.11 Static Variables vs. Global Variables
Global variable has no limits on manipulation
Static variable:
  Can only be modified by objects of one class
  Shared among all objects
  Associated with the class, not the object
class Transaction;
static int count = 0;
int id;
function new();
id = count++;
endfunction
endclass
Notes: 1) Lets say we want to create a variable that maintains a running count of the number of transaction that have been created. In this way we can track objects as they flow through a design. Since we cannot print out the address of an object this is a good way to debug a tesbench using an ID
2) One way is to use a global variable. Want to avoid global variables because they can be changed by code anywhere in the system, and may cause name conflicts.
3) A better way is to use a static variable. Lets look at how to accomplish this requirement with static variables.
When the class is declared count is set to 0. Only one copy of static variable count exists.
4) Variable id is not static and there will be a copy per object and is specific to each object.
5) When the first object of class Transaction is created the id is assigned the value of count and then count is incremented (post increment) to be ready for the next object creation.
6) Lets look at an example of creating objects using this class.

## Slide 21
5.11 Static/Global Variables (cont)
initial begin
Transaction t1, t2;
t1 = new();
$display("First id = %0d, count = %0d", t1.id, t1.count);
t2 = new();
$display("Second id = %0d, count = %0d", t2.id, t2.count);
end
# First id = 0, count = 1
# Second id = 1, count = 2
# First id = 0, count = 1
# Second id = 0, count = 1
If count was not declared as static:
Notes: 1) Note that the count variable is 2 because after the object pointed to by t2 is created the count has been post incremented twice.
2) If count was not declared as static there is a count variable allocated to each object. Every object allocated will have id =0 and count = 1;
3) Using the ID field is a good way to track objects as they flow through a design. When debugging a testbench, you often need a unique value. SystemVerilog does not let you print the address of an object, but you can make an ID field. Only a chandle can be printed in SV. We’ll talk about changle in Chapter 12.

## Slide 22
5.11.2 Accessing Static Variables.....
Only one copy of a static variable exists.
Static variables can be accessed through the class or handle
initial begin
Transaction t1, t2;
$display("1) Transaction::count = %0d", Transaction::count);
t1 = new();
$display("First id = 0d%0d, count = 0d%0d", t1.id, t1.count);
t2 = new();
$display("Second id = 0d%0d, count = 0d%0d", t2.id, t2.count);
$display("2) Transaction::count = 0d%0d", Transaction::count);
end
# 1) Transaction::count = 0d0
# First id = 0d0, count = 0d1
# Second id = 0d1, count = 0d2
# 2) Transaction::count = 0d2
Notes: 1) :: is called the class scope resolution operator. It determines what class variable count is from.
2) Note that I can print out the value of count before the objects have been created. Memory for static variables is allocated as soon as the class is declared.

## Slide 23
Static Variables Exercise
Using the previous MemTrans exercise create a static variable last_address that holds the initial value of the address variable from the most recently created object, as set in the constructor.
After allocating objects of class MemTrans (done in last exercise) print out the current value of last_address.
Notes: See Chap_5_Basic_OOP/exercise5 for complete code example.
class MemTrans;
logic [7:0] data_in; logic [3:0] address;
static logic [3:0] last_address;
function void print;
$display(“Data_in = %h, address = %h”, data_in, address);
endfunction
function new(logic [7:0] data_init = 0, logic [3:0] address_init = 0);
data_in = data_init;
address = address_init;
last_address = address;
endfunction
endclass
initial begin
MemTrans mt1, mt2;
mt1 = new(, .address_init(2));
mt2 = new(3, 4);
mt1.print;
mt2.print;
$display("last_address is %h", MemTrans::last_address); or $display("last_address is %h", mt2.last_address);
mt2 = null;
end

## Slide 24
class Transaction;
  static Config cfg;
endclass
initial begin
  Transaction::cfg = new(.num_trans(42));
end
5.11.3 Initializing static variables
Useful when every instance of a class needs info from an object of another class
A handle with static storage
Create a new config object.
and assign handle of new Config object to static handle cfg in class Transaction
Notes:   1) A static variable is usually initialized in the declaration.
2) Another use for a static variable is when every instance of a class needs information
from a single object of another class. A common occurrence. If the handle is not static every object will have it’s own copy, wasting space.
3) Lets assume that class Config has a variable called num_trans indicating the number of transaction to process.
4) In this example declare a static handle to class Config.
5) At initialization call class Config’s constructor through class Transaction (since it is static) and pass in the number of transaction to process, i.e. 42.

## Slide 25
5.11.4 Static Methods
Manipulating static variables with a method accessed with the class name requires a static method
# 3) Transaction.count = 1
class Transaction;
static int count = 0;
int id;
function new();
id = count++;
endfunction
static function void dec_count();
--count;
endfunction
endclass
Transaction::dec_count();
$display("3) Transaction.count = %0d", Transaction::count);
dec_count must be declared as static
Notes: 1) If you desire to manipulate static variables with a method called by the class name, not by the object, need to use a static method. The static variable can always be manipulated through 1) The handle or 2) the class without using a method.
2) Create a function called dec_count that decrements the static variable count.
3) Then add onto the previous example a call to this static function from the class name Transaction and print out the new value.
4) As you can see it is now 1 (decremented from 2 assuming 2 objects were created).

## Slide 26
Static Methods Exercise
Using the previous MemTrans exercise create a static method called print_last_address that prints out the value of static variable last_address
After allocating objects of class MemTrans, call the method print_last_address to print out the value of last_address
Notes: See Chap_5_Basic_OOP/exercise6 for complete code example.
2 ways to do assign to last_address, explicitly after each created object or in the constructor.
class MemTrans;
logic [7:0] data_in;
logic [3:0] address;
static logic [3:0] last_address;
function void print;
$display(“Data_in = %h, address = %h”, data_in, address);
endfunction
function new(logic [7:0] data_init = 0, logic [3:0] address_init = 0);
data_in = data_init;
address = address_init;
MemTrans::last_address = address;
endfunction
static function void print_last_address;
$display("last_address is %h", last_address);
endfunction
endclass
initial begin
MemTrans mt1, mt2;
mt1 = new(, .address_init(2));
mt2 = new(3, 4);
m1.address = 4’hF;
mt1.print;
mt2.print;
MemTrans::print_last_address; or mt2.print_last_address; <- don’t recommend this.
mt2 = null;
end
NOTE: Skip if low on time.

## Slide 27
5.12 Scoping Rules
int limit;
program automatic p;
  int limit;
  class Foo;
    int limit, array[];
    function void print (int limit);
    for (int i=0; i<limit; i++)
    $display(“%m: array[%0d]=%0d”, i, array[i]);
    endfunction
  endclass
  initial begin
  int limit = $root.limit;
    Foo bar;
    bar = new();
    bar.print(limit)
    bar.print(bar.limit);
end endprogram
Notes: 1) Be aware of what variable you are referencing.
2) limit is defined as a global variable, program variable, class variable, task variable, and local variable.
3) Determine which limit is used when referenced.
NOTE: Skip if low on time.

## Slide 28
5.12 Scoping Rules (cont)
program automatic test;
int i;
class Bad;
logic [31:0] data[];
function void display;
for (i=0;i<data.size(); i++)
$display(“data[%0d=%x”, i, data[i]);
endfunction
endclass
endprogram
SystemVerilog searches up the scopes for variables
Declare classes in a package.
Notes: 1) In this function where is i declared? Since it’s not declared in the for loop SystemVerilog searches up the scopes until it’s found. In this case it’s found declared in the program. If you never use i anywhere else this isn’t an issue but if you do use i elsewhere it’s value will be determined from the for loop. If you meant to declare a loop variable you want the compiler to flag an error.
2) Suggestion is to declare classes in a package. When you compile the package containing class Bad the compiler will report an error because it doesn’t know what i is. An example of this is in Sample 5.18
NOTE: Skip if low on time.

## Slide 29
5.12.1 What is this?
Keyword this allows unambiguous reference to class variables/methods, etc.
Commonly used in custom constructors where argument to constructor matches a class variable.
Lazy programming???
class Scoping;
  string oname;
  function new(string new_oname);
  oname = new_oname;
  endfunction
endclass
class Scoping;
  string oname;
  function new(string oname);
  this.oname = oname;
  endfunction
endclass
Notes: By naming the variable passed into the custom constructor to a unique name I don’t have to use this.

## Slide 30
5.13 Using one Class Inside Another
Objects of a class can be created inside another class
Enables reuse and is similar to composition
class Statistics;
time startT; // Transaction start time
static int ntrans = 0; // Transaction count
static time total_elapsed_time = 0;
function void start();
startT = $time;
endfunction
function void stop();
time how_long = $time - startT;
ntrans++; // Another trans completed
total_elapsed_time += how_long;
endfunction
endclass
Notes: 1) Objects of a class can be created inside another class just like modules are instantiated inside of other modules
2) Enables reuse because we can reuse the Base classes (using C++ naming) and is similar to composition which is discussed in chapter 8.
3) This is an example of our base Statistics class.
4) It will determine how long the simulation has been running with the start/stop functions and every time function stop is called will increment a class variable total_elapsed_time with the difference in time stored in local variable how_long. Lets see how this class is used in another class.

## Slide 31
Using Statistics inside another Class
class BusTran;
bit [31:0] addr, src, data[8], crc;
Statistics stats;
function new();
stats=new();
endfunction
task create_packet();
// Fill packet with data
stats.start();
...... // Transmit packet
stats.stop();
endtask
endclass
Notes: 1) Note that in the constructor for BusTran we create an object of class Statistics. Otherwise the handle stats would be null and the calls to start, stop, and how_long will fail.
2) We have used a base statistics class to keep track of how long a packet takes to transmit and how long the total transmit time is.
3) A basic rule is if you are typing the same code for different classes it’s time to create a base class and use it inside your classes.

## Slide 32
5.13.2 Compilation Order Issue
Compilation order of classes is not as lenient as modules
Example: two classes each need a handle to the other.
typedef class Statistics;
class Transaction;
Statistics stats;
endclass
class Statistics;
endclass
class Transaction;
Statistics stats;
endclass
class Statistics;
endclass
Invalid type 'Statistics'.
Notes: 1) Compilation order of classes is not as lenient as modules where they can be compiled in any order
2) Sometimes a class variable needs to be declared before the class itself has been declared. For example, if two classes each need a handle to the other.
3) Only do this if you really need to.
NOTE: Skip if low on time.

## Slide 33
Classes within Classes Exercise
Complete function print_all in class MemTrans to print out data_in and address using base class PrintUtilities. Demonstrate it’s usage.
class PrintUtilities;
function void print_4(input string name, input [3:0] val_4bits);
$display("%t: %s = %h", $time, name, val_4bits);
endfunction
function void print_8(input string name, input [7:0] val_8bits);
$display("%t: %s = %h", $time, name, val_8bits);
endfunction
endclass
class MemTrans;
bit [7:0] data_in;
bit [3:0] address;
PrintUtilities print;
function new(); print = new(); endfunction
function void print_all;
......
endfunction
endclass
Notes: See Chap_5_Basic_OOP/exercise7 for complete code example.
class MemTrans;
bit [7:0] data_in;
bit [3:0] address;
PrintUtilities print;
function new();
print = new();
endfunction // new
function void print_all;
print.print_8("data_in", data_in);
print.print_4("address", address);
endfunction // print_data_address
endclass
program automatic test;
import my_package::*;
initial begin
MemTrans mt1, mt2;
mt1 = new();
mt1.print_all;
mt1.print.print_8("data_in", mt1.data_in);
end
endprogram

## Slide 34
5.14.1 Passing objects/handles to methods
What happens when an object is passed to a method?
  The handle to the object is passed, not the object.
  A copy of the handle is made
gen
object of class Transaction
task transmit(input Transaction trans);
...........
endtask
trans
task generator;
Transaction gen;
gen =new;
transmit(gen);
endtask
Notes: 1) In section 5.14 Understanding Dynamic Objects.
2) Start with a task generator that creates new transaction objects.
3) Then call a task or function transmit and pass the handle of the object to the task or function.
4) A copy of the handle is created in task transmit called trans.
5) Two handles are created, both point to the same object.
6) If the handle in task transmit is modified it doesn’t affect the gen handle because it is a copy.
If you want to modify the handle gen pass the handle by reference (using the keyword ref).
But whether or not the ref keyword is used the object can be modified since the object was not passed, only the handle. If you don’t want the object modified, pass a copy, leaving the original unmodified which we’ll see in a few slides.

## Slide 35
function void create(Transaction tr);
tr = new();
tr.addr = 42;
.....
endfunction
Transaction t;
initial begin
  create(t);
  $display(t.addr);
end
5.14.2 Modifying a handle in a task
Specify ref on method arguments you want to modify
What does t point to?
tr cannot be modified
function void create(ref Transaction tr);
Notes: Use ref on method arguments you want to modify including handles.
Since the default direction is input tr cannot be modified which will occur when new() is called.
With the bug t =null and the display fails because there is no object that t points to.
With the correction 42 is displayed.
Note: If the arguments to the function are specified as an output ref is not required.

## Slide 36
task generator_bad(int n);
Transaction t;
t = new();
repeat (n) begin
    t.addr = $random();
    $display(“Sending addr = %h”, t.addr);
    transmit(t);
  end
endtask
5.14.3 Modifying Objects in Flight
Be sure to create a new object for each transaction
Otherwise every object could be the same
1 object shared by n transmit calls
Notes: 1) By in flight the authors mean objects are spawned in separate threads and the threads are not holding up the simulator. We’ll get to how to do this in chapter 7. The key to this issue is understanding that a transmit may take multiple clock cycles to complete.
2) If calling transmit takes 0 time how long will it take to call transmit n times? 0.
3) If we assume that calling transmit takes 1 or more clock cycles and that calling transmit does not hold up the repeat loop t.addr is randomized n times but only the final value of t.addr is used for all n threads of transmit. Essentially the values in the object are re-randomized in flight.
4) Difficult to debug because the display will show random addr values.
5) To fix this create n new objects.
NOTE: Assuming that the transmit task makes a copy of the handle (i.e. not passed by ref) you can recycle the same handle over and over. This is required since only 1 handle t is created. Remember that unless the handle is passed by ref the task/function makes a copy.

## Slide 37
task generator();
Transaction tarray[10];
foreach (tarray[i]) begin
tarray[i] = new();
transmit(tarray[i]);
end
endtask
5.14.4 Array of Handles
Your testbench might need to store and reference many objects
An array of handles is convenient for this.
Notes: Each element in the array points to an object.
Don’t attempt to do tarray = new(). This is a compile error. No way to call new on an entire array of handles.

## Slide 38
Objects and Handles Exercise
program automatic test;
import my_package::*;
initial begin
end
task generator
endtask
task transmit(Transaction tr);
.......
endtask // transmit
endprogram
Declare an array of 5 Transaction handles
Call a generator task to create the objects
Complete the generator task header
Create objects for every handle in the array and transmit the object.
Notes: See Chap_5_Basic_OOP/exercise8 for complete code example.
Complete the code as instructed
program automatic test;
import my_package::*;
initial begin
Transaction tarray[5];
generator(tarray);
end
task generator(ref Transaction gen_array[5]);
foreach (gen_array[i]) begin
gen_array[i] = new();
transmit(gen_array[i]);
end
endtask
task transmit(Transaction tr);
endtask // transmit
endprogram

## Slide 39
5.15 Copying Objects
Pass a copy of an object to a method to keep it from being modified
Any custom constructor is not called
Transaction src, dst;
initial begin
src = new();
src.stats.StartT=42;
src
id=0
stats
startT=42
src
id=0
stats
startT=42
dst
id=0
stats
96
class Transaction;
  bit [31:0] addr;
  static int count = 0;
  int id;
  Statistics stats;
function new();
stats = new()
id = count++;
endfunction
endclass
dst = new src;
dst.stats.StartT = 96;
Notes: 1) Using the new operator to copy an object results in a shallow copy which only copies the current object and variables. This is because any custom constructor is not called
2) src.stats.StartT=42; assigns to 42 the StartT variable in the class Statistics object pointed to by handle stats. This handle is in object src.
3) dst = new src; blindly copies src to dst. A new Transaction object is created, a new id, and a new stats handle but the custom constructor in class Transaction is not called. This means that even though a new stats handle is created a new Statistics object is not and the id is initialized to it’s default, 0. Both src.stats and dst.stats points to the single Statistics object.
4) When dst.stats.StartT = 96 is executed the value of StartT is changed to 96. Probably not what we want.
5) For all but the most trivial classes you should write your own copy function

## Slide 40
5.15.3 Writing a Deep Copy Function
class Transaction;
  bit [31:0] addr;
  static int count = 0;
  int id;
  Statistics stats;
  function new();
    stats = new();
    id = count++;
  endfunction
function Transaction copy();
    copy = new();
    copy.addr = addr;
    copy.stats = stats.copy();
  endfunction
endclass
class Statistics;
time startT;
function Statistics copy();
copy = new();
copy.startT = startT;
endfunction
endclass
Suggested for all but the most trivial classes
UVM data macros do this for you automatically!
Notes:     1) function Transaction copy(); Function copy returns a handle of type Transaction;
    2) copy = new(); creates an object of type Transaction and also calls the custom constructor so a Statistics object also gets created.
    3) copy.addr = addr; copy all the data values
    4) copy.stats = stats.copy(); call the copy function of the Statistics class.
    5) The Statistics copy function is very simple and is what your copy function will probably look like initially.
6) UVM data macros create the copy function automatically. Manually creating the copy function is very error prone, especially when you add new variables. Forget one and your copy function is incomplete.

## Slide 41
5.15.3 Using the Deep Copy Function
Transaction src, dst;
initial begin
src = new();
src.stats.StartT=42;
dst = src.copy();
dst.stats.StartT = 96;
end
src
id=0
stats
startT=42
dst
id=1
stats
startT=42
src
id=0
stats
startT=42
src
id=0
stats
startT=42
dst
id=1
stats
startT=96
Notes:     the only difference here is that we call the Transaction class copy function which calls the Statistics class copy function and the class is perfectly copied. If you don’t have classes inside of classes you might be temped to not write a copy function but if your testbench evolves to a point that you need a class inside of a class you will have to write lots of copy function and replace the appropriate new() with copy(). Testbenches have a habit of getting more complex than initially planned.

## Slide 42
Copy Exercise
For the following class create a copy function and demonstrate its usage. Assume the Statistics class has its own copy function.
package automatic my_package;
class MemTrans;
bit [7:0] data_in;
bit [3:0] address;
Statistics stats;
function new();
data_in = 3;
address = 5;
stats = new();
endfunction
endclass;
endpackage
Notes: See Chap_5_Basic_OOP/exercise9 for complete code example.
package automatic my_package;
class MemTrans;
bit [7:0] data_in;
bit [3:0] address;
Statistics stats;
function new();
data_in = 3;
address = 5;
stats = new();
endfunction
function MemTrans copy();
copy = new();
copy.address = address;
copy.data_in = data_in;
copy.stats = stats.copy();
endfunction // copy
function void print();
$display("Data_in = %h, address = %h", data_in, address);
endfunction
endclass;
endpackage
usage: initial begin
MemTrans mt1, mt2, mt3;
mt1 = new();
mt2 = new mt1;
mt3 = mt1.copy();

## Slide 43
5.17 Public vs Local
C++/Java
  All variables in a class are local by default
  Classes provide accessor functions to allow access.
  Long term software stability is paramount.
SystemVerilog
  All variables in a class are public by default
  Variables can be labeled local or protected.
  Tradeoff between software stability and flexibility.
Notes: In C++/Java all variables in a class are local unless labeled otherwise.
Classes provide accessor functions to allow access to the local variables. In this way only the variables the class expects to be changed can be changed.
A member variable identified as local is available only to methods inside the class.
The only difference between local and protected is that local variables are not visible to classes that are derived (or extended) from the class with the local variable. This means that if I have a base class, PrintUtilities with a local variable a class derived from it cannot access the local variable.
Classes with protected variables are visible even to derived classes.
With testbenches want the flexibility to, for example, inject errors. If any variable to do this were local or protected accessor functions would need to be written which makes the testbench larger and more complex.
It’s a tradeoff.

## Slide 44
5.18 Building a Testbench
Notes: 1) Each of these blocks is an object of a class that is designed as a transactor. A transactor simply receives a transation object from a previous block, makes some transformations, and sends it to the following object. Obviously, one block needs to create the initital transaction and this is the generator object.
2) One thing we haven’t talked about is how to exchange transactions between blocks. In chapter 7 we’ll learn how to use mailboxes which are fifo’s with the ability to stall a thread until a new value is placed in the mailbox. for now think of classes as powerful structures. Classes are required for SystemVerilog’s constrained randomization features which we’ll learn about next in chapter 6